## Slide 1: LOCATION
RECONSTRUCTION OF GREEN ROAD STAFF QUARTER
Group 2
Reconstruction of Green Road Staff Quarter
1

## Slide 2: LOCATION
Green Road, Dhanmondi, Dhaka-1205
Google Map- 23°44'46.6"N 90°22'59.2"E
Group 2
Reconstruction of Green Road Staff Quarter
2

## Slide 3
Most of the buildings are old and fragile
Buildings are closely placed
CURRENT SCENARIO
No dedicated parking facility

## Slide 4
Poor condition of the sports arenas
Unhygienic and poor drainage situation
No proper waste management system

## Slide 5
CURRENT SCENARIO
Group 2
Reconstruction of Green Road Staff Quarter
5
27 Buildings
2 Sport Field
1 Mosque
0 pond
Project area 0.5 km2
500 Family

## Slide 6
STAKEHOLDERS
Group 2
Reconstruction of Green Road Staff Quarter
6
Government Officials (PWD)
Current Residencies
Shop Owners Near the Project
People Living Near the Project
Representatives from Green Life Hospital and Modern Hospital

## Slide 7
Chart: 
| 1st Qtr | 3rd Qtr | 4th Qtr
Sales | 0.82 | 0.17 | 0.01
Necessity for the Inclusion of Sports Field and Playground within the Facility
Chart: 
| 1st Qtr | 3rd Qtr | 4th Qtr
Sales | 0.72 | 0.2 | 0.08
Waste Management System of the Area
Chart: 
| 1st Qtr | 3rd Qtr | 4th Qtr
Sales | 0.84 | 0.11 | 0.05
Current Residential Facilities of the Quarter is Satisfactory or Not
STAKEHOLDER SURVEY
Unsatisfactory
Neutral
Satisfactory
Chart: 
| 1st Qtr | 3rd Qtr | 4th Qtr
Sales | 0.92 | 0.08 | 0
Condition and Safety of Internal Roadway System
Chart: 
| 1st Qtr | 3rd Qtr | 4th Qtr
Sales | 0.86 | 0.05 | 0.09
Condition and Positioning of Existing Buildings
Chart: 
| 1st Qtr | 3rd Qtr | 4th Qtr
Sales | 0.61 | 0.32 | 0.07
Parking Facilities inside the Staff Quarter
Group 2
Reconstruction of Green Road Staff Quarter
7

## Slide 8: PROJECT OBJECTIVE
Upgrade plumbing infrastructure for proper water management.
Enhance overall living conditions and hygiene standards.
Optimize space utilization through taller, consolidated structures.
Implement efficient waste management systems.
Improve parking infrastructure and accessibility.
Renovate sports arenas for community use and enjoyment.
OBJECTIVES
Enhance green spaces and landscaping for a healthier environment.
Group 2
Reconstruction of Green Road Staff Quarter
8

## Slide 9
PROPER ORIENTATION OF BUILDING
OPEN AND GREEN SPACE AREA
1
HIGH RISE BUILDING
13 STORIED BUILDING
(WITH BASEMENT)
4 UNIT APARTMENT (DIFFERENT SIZE)
DEDICATED PARKING FACILITY
2
MASTER PLAN
MODELING
SPECIFIC GOALS
Group 2
Reconstruction of Green Road Staff Quarter
9

## Slide 10
STEP
01
STEP
03
STEP
05
STEP
02
STEP
04
PWD Office
WASA
City corporation
Survey
Soil Report
Data Collection
Preliminary
Design
Financial & Economic Analysis
Evaluation of Alternative Analysis
EIA
Draft Master Plan
Draft Floor Plan
Components Size
Preliminary Cost Analysis for Alternatives
Alternative Design Analysis
ACTIVITY OUTLINE
Group 2
Reconstruction of Green Road Staff Quarter
10

## Slide 11
STEP
06
STEP
08
STEP
10
STEP
07
STEP
09
Detail Design & Analysis
Tendering
Opening &
Operation
Construction
& Quality
Control
Bill of Quantity
ETABS Modeling
RCC Design
Water Reservoir & Septic Tank Design
Plumbing and Drainage
ACTIVITY OUTLINE
Group 2
Reconstruction of Green Road Staff Quarter
11

## Slide 12: SURVEY AND DATA
Traffic Data Collection and Analysis
Chart: Traffic Data Comparison
| Gate 1 | Gate 2 | Gate 3
Present | 19 | 14 | 25.25
Future | 26 | 19.6 | 35.5
Group 2
Reconstruction of Green Road Staff Quarter
12

## Slide 13
Soil Test Report Collection, Summarizing and Analysis
SURVEY AND DATA
0 meter
18 meter
9 meter
Stiff Clay
Dense Sand
Group 2
Reconstruction of Green Road Staff Quarter
13

## Slide 14: MASTER PLAN
Group 2
Reconstruction of Green Road Staff Quarter
14

## Slide 15: MASTER PLAN
Playground
Residential Buildings
Outside Parking
Garden
Pond
Mosque
Outside Parking
Community Centre
Field
Total plan area = 5,43,660 sft
Four Different Zones
z-1 -> 1500 sft
z-2 -> 1200 sft
z-3 -> 1000 sft
z-4 -> 800 sft
Building to building distance = 70ft
Mosque floor area = 5166 sft
Community Centre floor area = 6835 sft
Group 2
Reconstruction of Green Road Staff Quarter
15

## Slide 16
Baseline environment: Physicochemical
40%
60%
20%
Baseline environment: Ecological environment
Baseline environment: Socio-economic environment
“RED” category project => EIA required
Baseline Environment study
Baseline environment: Physicochemical
Baseline Environment : Physicochemical
Group 2
Reconstruction of Green Road Staff Quarter
16
ENVIRONMENTAL IMPACT ASSESSMENT

## Slide 17: PRE-CONSTRUCTION STAGE
ENVIRONMENTAL IMPACTS
SOLID WASTE
UNDERGROUND GAS PIPELINE
CUTTING OF TREES
ENVIRONMENTAL IMPACT AND MITIGATION MEASURE
MITIGATION MEASURES
PROPER SOLID WASTE MANAGEMENT
SHIFTING THE GAS LINES
TREE PLANTATION AFTER CONSTRUCTION
Group 2
Reconstruction of Green Road Staff Quarter
17

## Slide 18: CONSTRUCTION STAGE
ENVIRONMENTAL IMPACTS
AIR AND SOUND POLLUTION
BLOCKAGE TO DRAINAGE
TRAFFIC CONGESTION
IMPROPER MANAGEMENT OF
SEWAGE WASTE
MITIGATION MEASURES
EMISSION CONTROL DEVICE AND NOISE CONTROL KITS
ENSURE 3R (REDUCE, REUSE, RECYCLE)
DELIVERY OF MATERIALS AT OFF PEAK HOUR
PROPER SANITATION AND OTHER FACILITIES
ENVIRONMENTAL IMPACT AND MITIGATION MEASURE
Group 2
Reconstruction of Green Road Staff Quarter
18

## Slide 19: RESETTLEMENT AND DISASTER RESILIENCE
Resettlement Issue
Will be given money for relocation
Legal consideration from government
Transportation facilities or corresponding money
Disaster Resilience of the Project Site
Disaster Risk Reduction measures
Elevation of the area
High strength steel and concrete will be used
Bare land will be surrounded with greeneries
Group 2
Reconstruction of Green Road Staff Quarter
19

## Slide 20: Typical Floor Plan
Typical Floor Plan Details:
Total Area = 7090 sft
Common Space Area= 1090 sft
Number of Apartment = 4
For each apartment :
• 3 Bedrooms
Room 1 : 12’-1”X13’-4”
Room 2: 10’-0”X14’-7”
Room 3: 12’-1”X13’-4”
• 4 Toilets
• 1 Dining Room : 13’-6”X12’-0”
• 2 Living Rooms
• 1 Kitchen : 9’-2” X9'-2”
• 3 Verandas
Number of stair in building = 2
Number of lifts in building = 2
Size of lift : 7’-11”X10’-0”
TYPICAL FLOOR PLAN
Group 2
Reconstruction of Green Road Staff Quarter
20

## Slide 21
ANALYSIS OF ALTERNATIVES
Alternatives | Cost |  | Design |  | Material Availability |  | Aesthetic |  | Qualitative Comparison |  | Total
 | Weightage | Score | Weightage | Score | Weightage | Score | Weightage | Score | Weightage | Score | 
Type A | 0.3 | 80 | 0.2 | 80 | 0.15 | 80 | 0.2 | 70 | 0.15 | 80 | 78
Type B | 0.3 | 60 | 0.2 | 70 | 0.15 | 80 | 0.2 | 80 | 0.15 | 90 | 73.5
Beam supported slab
Mat foundation
.
Flat Plate
Pile Foundation
TYPE A
TYPE B
Group 2
Reconstruction of Green Road Staff Quarter
21

## Slide 22: 4
FLEXIBLE (T>1S)
SEISMIC ZONE
ZONE-02 (DHAKA)
ZONE COEFFICIENT=0.20
OCCUPANCY CATEGORY
EXPOSURE
CATEGORY
BUILDING TYPE
OC-02
(RESIDENTIAL)
IMPORTANCE FACTOR=1.0
CATEGORY-A (URBAN AREA)
DESIGN BASIS
2
3
4
1
Group 2
Reconstruction of Green Road Staff Quarter
22

## Slide 23: DESIGN BASIS
SITE CLASS
SC
Group 2
Reconstruction of Green Road Staff Quarter
23

## Slide 24: DESIGN BASIS
SEISMIC DESIGN CATEGORY
SDC-C
SEISMIC FORCE RESISTING SYSTEM
IMRF+SHEAR WALL
Group 2
Reconstruction of Green Road Staff Quarter
24

## Slide 25: MODELING PARAMETERS
Group 2
Reconstruction of Green Road Staff Quarter
25

## Slide 26: MODEL FOR ANALYSIS
Group 2
Reconstruction of Green Road Staff Quarter
26

## Slide 27
1
2
3
4
6
5
SERVICEABILITY ANALYSIS
BEAM DEFLECTION
(SHORT TERM AND LONG TERM)
WIND SWAY
WIND DRIFT
EQ DRIFT
TORSIONAL IRREGULARITY
SLAB DEFLECTION
(SHORT TERM AND LONG TERM)
Group 2
Reconstruction of Green Road Staff Quarter
27

## Slide 28
STAIR
SHEAR WALL
MAT.
BASEMENT WALL
SLAB
COLUMN
BEAM.
DESIGN COMPONENTS
COMPONENTS
1
2
3
4
5
6
7

## Slide 29: SIZE OF COMPONENTS
Thickness = 7”
Size = 15”x24”
C1 = 18”x24” C2 = 20”x30”
Thickness = 41’’
Slab
Column
Beam
Mat
Group 2
Reconstruction of Green Road Staff Quarter
29

## Slide 30
BEAM DESIGN
Longitudinal Reinforcement Calculation:
Main Bar Calculation at Middle, Left Corner, Right Corner from ETABS Data
Temperature and Shrinkage Reinforcement Calculation
STEP #1
STEP #2
Transverse Reinforcement Calculation :
Shear Reinforcement Value
from ETABS
Provided Tie Bar Spacing According to IMRF
Group 2
Reconstruction of Green Road Staff Quarter
30

## Slide 31
BEAM DESIGN
Beam Size – 15’’ x 24’’
3rd Floor
ETABS :
Stiffness Modifier : 0.35 and 0.0001
Group 2
Reconstruction of Green Road Staff Quarter
31

## Slide 32
COLUMN DESIGN
Longitudinal Reinforcement:
Minimum Steel for Temperature and Shrinkage
Required Steel from ETABS Data
Compared and Provided Necessary Rebar
STEP #1
STEP #2
STEP #3
STEP #4
Tie Reinforcement:
16 * Dia of main bar
48 * Dia of Tie Bar
Least Dimension of Column
IMRF Requirements for L0:
Larger of C1 and C2
Clear Span / 6
18”
IMRF Requirements for Ties :
8 x Smallest Longitudinal Bar Diameter
24 x Tie Bar Diameter
0.5 x Smaller of C1 or C2
Group 2
Reconstruction of Green Road Staff Quarter
32

## Slide 33
COLUMN DESIGN
C1
EXTERIOR COLUMNS
18’’ x 24’’
C2, C3
INTERIOR COLUMNS
20’’ x 30’’
C1
Base – 2F
3F – 10F
11F – 12F
C2
C3
Base – 2F
3F – 10F
11F – 12F
Base – 5F
6F – 10F
11F – 12F
Group 2
Reconstruction of Green Road Staff Quarter
33

## Slide 34
COLUMN DESIGN
CROSS SECTIONS OF C1,C2,C3 COLUMNS
5
10
Group 2
Reconstruction of Green Road Staff Quarter
34

## Slide 35
SLAB DESIGN
Minimum Reinforcement Calculation:
Required Reinforcement: 0.15 in2/ft
Spacing 10”
STEP #1
STEP #2
Extra Reinforcement from ETABS
Group 2
Reconstruction of Green Road Staff Quarter
35

## Slide 36
SLAB DESIGN
Slab Reinforcement X Direction
Slab (X-direction)
#4 straight bar @10” c/c for both CS and MS
#4 extra top @10” c/c for CS
#4 extra top @10” c/c for CS
#4 extra bottom @10” c/c for MS
#4 extra bottom @10” c/c for MS
Group 2
Reconstruction of Green Road Staff Quarter
36

## Slide 37
SLAB DESIGN
Slab Reinforcement Y Direction
Slab (Y-direction)
#4 straight bar @10” c/c for both CS and MS
#4 extra top @10” c/c for CS
#4 extra top @10” c/c for CS
#4 extra bottom @10” c/c for MS
#4 extra bottom @10” c/c for MS
Group 2
Reconstruction of Green Road Staff Quarter
37

## Slide 38
MAT FOUNDATION
Minimum Reinforcement Calculation:
Required Reinforcement: 0.89 in2/ft
Using #8@8”C/C
STEP #1
STEP #2
Extra Reinforcement from ETABS:
Stiffness Modifier: 0.25
Group 2
Reconstruction of Green Road Staff Quarter
38

## Slide 39
MAT FOUNDATION
Mat Foundation Reinforcement X Direction
X- direction:
#8@8”c/c - bottom
#8@8”c/c - top
#10@8”c/c - extra top
#10@10”c/c - extra bottom
Group 2
Reconstruction of Green Road Staff Quarter
39

## Slide 40
MAT FOUNDATION
Mat Foundation Reinforcement Y Direction
Y- direction:
#8@8”c/c - bottom
#8@8”c/c - top
#7@12”c/c - extra top
#7@10”c/c - extra bottom
Group 2
Reconstruction of Green Road Staff Quarter
40

## Slide 41: WATER DEMAND CALCULATION
Water Demand As per BNBC 2020
Peak Factor:
Domestic = 2.5
Mosque = 4
Community Center = 4
Time Factor:
Domestic= 24/24 = 1
Mosque = 24/24 = 1
Community Center = 24/(2X6) = 2
Domestic =180 lpcd
Mosque=75 lpcd
Community Center=
90 lpcd
Group 2
Reconstruction of Green Road Staff Quarter
41

## Slide 42: WATER DEMAND CALCULATION
Facility Type | Building Size (sft) | Water consumption BNBC 2020 (lpcd) | Water Demand (Mlpd)
Domestic | 1500 | 180 | 0.742
 | 1200 | 120 | 0.424
 | 1000 | 120 | 0.354
 | 800 | 80 | 0.236
Mosque | 3000 | 75 | 0.900
Community centre | 1000 | 90 | 0.720
Fire Hydrant | - | - | 0.291
Fire fighting | - | - | 0.540
Total Demand (Mlpd) |  |  | 4.206
Group 2
Reconstruction of Green Road Staff Quarter
42

## Slide 43: WATER RESERVOIR
Type | Quantity | Dimension | Capacity
Under Ground Water Reservoir (Daily Use) | 2 | 22’x15’x10’ | 6710 cft
Under Ground Water Reservoir (Firefighting) | 1 | 15’x8’x10’ | 1100 cft
Over Head Water Tank | 2 | 15’x12’x10’ | 3500 cft
Septic Tank | 2 | 34’x11.2’x4.3’ | Sludge storage zone 0.19 m Sludge digestion zone 0.143 m Scum storage zone 0.076 m Sedimentation zone 0.599 m
Group 2
Reconstruction of Green Road Staff Quarter
43

## Slide 44: PLUMBING
BRANCH LAYOUT
fIgURE: branch layouT
PLUMBING
Group 2
Reconstruction of Green Road Staff Quarter
44

## Slide 45
WATER SUPPLY ELEVATION
fIgURE : WATER SUPPLY ELEVATION OF BUILDING
Group 2
Reconstruction of Green Road Staff Quarter
45

## Slide 46: Soil branch
soil branch
DRAINAGE
Group 2
Reconstruction of Green Road Staff Quarter
46

## Slide 47: Waste branch
waste branch
WASTE branch
DRAINAGE
Group 2
Reconstruction of Green Road Staff Quarter
47

## Slide 48: Vertical pipes
Soil Vent Stack dia 75mm
Waste Stack dia 125mm
Soil Stack dia 100mm
Waste Vent Stack dia 100mm
GL
Main Sewer
10’
6.5’
12F
VERTICAL PIPES
Group 2
Reconstruction of Green Road Staff Quarter
48

## Slide 49
COST ANALYSIS
ASSOCIATED COST
AND BENEFIT
PROJECT LIFETIME
(50 YEARS)
8.2%
FIRR
14%
EIRR
DR<IRR BCR>1
INDICATOR
FINANCIAL AND ECONOMIC ANALYSIS
Group 2
Reconstruction of Green Road Staff Quarter
49

## Slide 50
FINANCIAL AND ECONOMIC ANALYSIS
BCR=0.60
BCR=1.20
NOT FINANCIALLY
VIABLE
ECONOMICALLY
VIABLE
Financial Analysis
Economic Analysis
DR=12%
Group 2
Reconstruction of Green Road Staff Quarter
50

## Slide 51
01
CASH INFLOW
02
CASH OUTFLOW
03
DISCOUNT RATE
01
EXPECTED CASE
02
PESSIMISTIC CASE
03
OPTIMISTIC CASE
VARIABLES CONSIDERED
CASES CONSIDERED
BASE CASE
COST BENEFIT
COST BENEFIT
SENSITIVITY ANALYSIS
Group 2
Reconstruction of Green Road Staff Quarter
51

## Slide 52
11.6%
12.6%
12.7%
14%
ACTUAL COST AND BENEFIT
1
BENEFIT 10%
3
COST 10%
2
COST 10%
+
BENEFIT 10%
4
EIRR VALUES
SENSITIVITY ANALYSIS
COMPARATIVE ANALYSIS FOR PESSIMISTIC CASE
Group 2
Reconstruction of Green Road Staff Quarter
52

## Slide 53
EARTHWORK EXCAVATION
SLAB
STAIR
LINTEL
SUNSHADE
COLUMN
12
11
10
9
8
7
6
5
4
3
2
1
MAT FOUNDATION
FLOOR TILES
BRICKWORK
TIMBER (DOOR FRAME)
SHEAR WALL
BEAM
0.27%
8.87%
20.89%
1.13%
1.63%
0.62%
8.6%
9.45%
6.23%
3.01%
4.93%
1.8%
BILL OF QUANTITY
COST PERCENTAGE ANALYSIS
Group 2
Reconstruction of Green Road Staff Quarter
53

## Slide 54
TIMBER (DOOR SHUTTERING)
SKIRTING
OHWT
PLUMBING
PAINTING
ALUMINIUM WINDOW FRAME
24
23
22
21
20
19
18
17
16
15
14
13
GLASS WORK
PLASTERING
SEPTIC TANK
MISCELLANEOUS
UWGR
RETAINING WALL
0.46%
0.13%
1.05%
3.24%
0.49%
6.39%
1.35%
3.96%
5.02%
0.88%
0.49%
8.6%
BILL OF QUANTITY
COST PERCENTAGE ANALYSIS
Group 2
Reconstruction of Green Road Staff Quarter
54

## Slide 55
37 Crore
BDT
3225 BDT
Cost Per
Building
BILL OF QUANTITY
Cost Per
Square Feet
Group 2
Reconstruction of Green Road Staff Quarter
55

## Slide 56
Cost for Resettlement Concern
Demolishing Cost
Parking Facility Development Cost
Construction cost of 16 Buildings
Renovation Cost of Community space
COMPONENTS OF TOTAL PROJECT COST
Cost of Green area and field Development
510 Crore BDT
Group 2
Reconstruction of Green Road Staff Quarter
56

## Slide 57
1
2
3
4
9
8
7
6
Instructions to Tenderers
Tender Data Sheet
General Conditions of Contract.
Particular Conditions of Contract
Tender & Contract Forms
Drawings
Particular Specifications
General Specifications
Bill of Quantities.
TENDER DOCUMENT
5
Group 2
Reconstruction of Green Road Staff Quarter
57

## Slide 58
IMPLEMENTATION TIMELINE

## Slide 59
THEORY BASED FORMULATION
SUPERSTRUCTURE AND SUBSTRUCTURE ANALYSIS
K4
DEPTH OF ENGINEERING KNOWLEDGE REQUIRED
K3
ANALYZE FOUNDATION TYPE
REACH CONCLUSIVE DECISION
K5
DESIGN OF FLOOR PLAN
DESIGN OF PLUMBING SYSTEM
DESIGN OF STRUCTURAL SYSTEM
P1
RANGE OF COMPLEX ENGINEERING PROBLEM
Group 2
Reconstruction of Green Road Staff Quarter
59

## Slide 60
P5
P4
P3
MASTER PLAN PREPARE
ABSTRACT THINKING
DEPTH OF ANALYSIS REQUIRED
FAMILIARITY OF ISSUES
DEMOLISHING BUILDINGS
ENVIRONMENTAL IMPACT
RESETTLEMENT CONCERN
RANGE OF COMPLEX ENGINEERING PROBLEM
EXTENT OF CODES
BNBC 2020
EURO CODE
Group 2
Reconstruction of Green Road Staff Quarter
60

## Slide 61
Thanks for Listening with great patience